## Slide 1
Design and Prototype of an Autonomous Shopping Cart
Siddharth Kurwa, Cockrell School of Engineering, siddharth.kurwa@gmail.com, Fall 2018
Control System Architecture
Background
Obstacle Avoidance Logic
Distributed Computing over I2C Network
Left Motor
Encoder Feedback
PID
Right Motor
Encoder Feedback
-
+
+
Gyro Feedback
Proximity Sensor Array
Disturbance
+
-
+
-
PID
Setpoint Selector
Project Goals
Mechanical Design
Further Information
CAD, source code, BOM, documentation: https://github.com/skurwa/smart-cart
To learn more about Sid: https://skurwa.github.io
Acknowledgements
I deeply appreciate Dr. Carolyn Seepersad’s support of this project. Her advice and feedback were beneficial to the completion of this project.
Conclusions and Future Work
2
4
3
5
6
1
7
9
Obstacle
8
PID controller,
Arduino Mega (master),
Polling at 50 Hz
Right wheel velocity measurement and motor drive,
Arduino Nano (slave)
Interrupt-based
Left wheel velocity measurement and motor drive,
Arduino Nano (slave),
Interrupt-based
Proximity sensor measurement and setpoint determination,
Arduino Nano (slave),
Polling at 4 Hz
Wheel velocity setpoints
Measured
velocity
Right wheel drive signal
Measured
velocity
Left wheel drive signal
Sealed lead acid battery
Ultrasonic proximity sensors
DC gearmotor
Grocery storage
Arduinos
Motor driver
Cart approaches obstacle and forward proximity sensors detect obstacle.
Cart performs a 90° turn using gyro feedback.
Cart moves forward until rear right proximity sensor crosses obstacle.
Cart performs a -90° turn using gyro feedback.
Cart moves forward until rear right proximity sensor crosses obstacle.
Cart performs -90° turn using gyro feedback.
Cart moves forward until rear right proximity sensor detects obstacle.
Cart performs a 90° turn using gyro feedback.
Cart moves forward along initial path.
The device design was modeled on a differential drive robot with one driven caster and two driving wheels. The controllers, power storage, and drive units are all stored on the bottom platform to maximize usable grocery storage volume. This functional prototype has a wooden construction and uses 3D-printed brackets, fixtures, and mounting adapters.
At a normal walking speed of 5 ft/s, each encoder clicks at a 3500 Hz frequency. Further, each proximity sensor requires a minimum 50 ms delay as its operation is limited by the speed of sound. If these tasks were handled serially by a single controller, the PID loop rate would be extremely limited by the high controller transport delay. To improve dynamic system stability and response time with changing setpoints, computational tasks were distributed over 4 Arduino microcontrollers and communicated over I2C protocol. By managing tasks in parallel to minimize transport delay, the system achieved a 50 Hz PID loop rate.
Closed-loop speed control is achieved with encoder feedback of each motor. However, motor speed differential is insufficient to determine heading of the system in slip conditions. Therefore, a gyro provides closed-loop heading control.
The functional prototype demonstrates the basic features required of a fully-functional autonomous shopping cart. The primary project goals have been achieved as the system is capable of performing obstacle avoidance, carrying groceries, and carries sufficient onboard processing power to enable further testing of further features.
Improvements to make to the existing system:
Add a bearing on a pillow-block between the motor and wheel hub. This will reduce the bending moment and shear load that the motors currently react and increase the maximum load-bearing capacity.
Mount ultrasonic sensors on a continuous servomotor or use LiDAR to provide 360° proximity detection. In the existing system, there are several “blind-zones” that are not monitored for potential obstacles.
Develop and implement more functional avoidance algorithms to allow smoother path-planning around obstacles rather than the combination of 90° turns and straight-line motion.
New features to incorporate:
Investigate indoor localization sensing capabilities. Several off-the-shelf options exist including PixyCam, bluetooth transmitters/receivers, and Wi-Fi.
RFID sensors and onboard payment terminals to enable monitoring of items in the cart and simplify the payment process.
References
Zafari, F., Gkelias, A., & Leung, K. K. (2018). A Survey of Indoor Localization Systems Technologies
(Rep. No. 1709.01015). https://arxiv.org/pdf/1709.01015.pdf
[PLACEHOLDER FOR PID TUNING IMAGES]
To tune the motor PID controllers, the Ziegler-Nichols tuning method was used. This method allows for experimental determination of the PID parameters (KP, KI, and KD) to maximize response time and eliminate steady-state error while maintaining system stability.
Semester goals:
Long-term goals:
To tune the motor PID controllers, the Ziegler-Nichols tuning method was used. This method allows for experimental determination of the PID parameters (KP, KI, and KD) to maximize response time and eliminate steady-state error while maintaining system stability.